Setup
Assemble the crazyflie
https://www.bitcraze.io/getting-started-with-the-crazyflie-2-0/
1. Follow the instructions to assemble the quadcopter (although it is probably already assembled)
2. Download the appropriate software for your computer/ mobile phone. The recommended way is installing the crazyflie virtual machine, but installing the software on Linux also works (note: windows doesn’t provide development capability)
  - For the virtual machine
    - first download virtual box from https://www.virtualbox.org/wiki/Downloads. Also download the extension pack – this is necessary to enable USB support.
    - Then download the crazyflie virtual machine from bitcraze https://github.com/bitcraze/bitcraze-vm/releases/.
    - Double click the “Update all projects” desktop icon to pull the most recent version of the Github code to your computer.
    - Download the appropriate USB driver for the crazyradio for the OS the virtual machine is being run on
      - For windows: https://wiki.bitcraze.io/doc:crazyradio:install_windows_zadig
  - For Linux
    - install info: https://github.com/bitcraze/crazyflie-clients-python/blob/master/README.md.
    - Main firmware: https://github.com/bitcraze/crazyflie-firmware.
    - Communicate with the drone: https://github.com/bitcraze/crazyflie-lib-python
Configure the Client
  - Start the Crazyflie client
  - Configure your Input Device
    - Xbox360: plug in, it should recognize it
    - HTC Vive controller
      - This takes more work – see setup the lighthouse
Fly the Crazyflie with controller
Right click the usb botton on the bottom right of the VM screen (or in settings) and check both the Radio PA and your controller (otherwise the VM can’t see those things plugged into the USB port) have a check mark next to them.

- Open the Crazyflie client inside the virtual machine (there should be a desktop shortcut)
  - Click scan, hopefully your drone will appear
  - Click connect to connect to the drone
  - Use the controller to fly the drone
- You may need to update the crazyflie firmware.
  - Get the file
    - Option A: Download the latest version from bitcraze, and keep it as a zip file on your computer https://github.com/bitcraze/crazyflie-release/releases.
    - Option B: If you have modified the firmware, and used the “make” command to compile it, it should be stored as cf2.bin inside projects/crazyflie-firmware
  - Press the power button on the crazyflie for three seconds to turn it on in bootloader mode. You should be disconnected from the drone.
  - Go to Connect → bootloader mode. Select the package to flash (probably one of the ones mentioned above) and then click “initiate bootloader cold boot”. Then click “program”.

Setup the Lighthouse deck
Install the following
- Install Python 2.7+ or 3.5+
- Install HTC Vive Stream: https://store.steampowered.com/about/ (you will have to create an account).
  - Once installed, open Steam and navigate to Library > Tools and scroll down until you find SteamVR. Double-click on SteamVR, select your install path and then hit the Next button
Configure SteamVR to work without a headset
Locate this configuration file <Steam Directory>/steamapps/common/SteamVR/drivers/null/resources/settings/default.vrsettings and open it with a text editor
    - Change “enable” to true and save the file
Locate this configuration file <Steam Directory>/steamapps/common/SteamVR/resources/settings/default.vrsettings
    - Change the “requireHmd” key under “steamvr”, to “false”
    - Change the “forcedDriver” key value to “null”.
    - Change the “activateMultipleDrivers” key value to “true”.
    - Save and close the file
Download the crazyflie firmware to the steamVR computer https://github.com/bitcraze/crazyflie-firmware
    - open a command line window and navigate to the Crazyflie firmware.
    - Run python3 -m pip install openvr
Resources:
https://wiki.bitcraze.io/doc:lighthouse:setup
http://help.triadsemi.com/articles/836917-steamvr-tracking-without-an-hmd

Using the Lighthouse deck
Get the position of the two bases
- Launch SteamVR
  Troubleshooting:
    - if it requires you to connect a headset, then repeat the configuration to work without a headset step above.
    - Without an HMD the master base station (the one in Mode B) will be at the origin of the space.
- Navigate to crazyflie-firmware/tools/lighthouse and run python3 get_bs_position.py
- This should produce some lines of code, with the position of the lighthouse bases, resembling the following. Copy the last two lines of code.

Inside the bitcraze VM or the bitcraze client (whichever you are using) navigate to crazyflie-firmware/src/deck/drivers/src, open lighthouse.c and paste these two lines in place of whatever is insider the baseStationsGeometry[] function. Also comment out the line #define DISABLE_LIGHTHOUSE_DRIVER.

The steamVR can be closed, and the VR kit unplugged. The crazyflie radio should be plugged in.

Compile and upload the firmware
- Navigate to crazyflie-firmware in the terminal and run the command make
- Upload the file crazyflie-firmware/cf2.bin to all drones
  Troubleshooting
    - If you are not using the bitcraze VM, various things must be installed (see the readme file https://github.com/bitcraze/crazyflie-firmware)
Verify positioning
- Go into the plotter tab (which can be enabled using View→ Tabs → Plotter)
- The safest way to verify the orientation of the space is to look at the estimated position. In the client you can create a new log block in “settings/logging configuration” containing “stateEstimate.x/y/z”.
- The positions from the state estimate x y z should correspond to the global x y z

crazyflie for ROS
http://wiki.ros.org/crazyflie
https://github.com/whoenig/crazyflie_ros

Useful Resources